## Slide 1
The Best Value in Electronic Test & Measurement

## Slide 2
SDS5000X
Introduction
Features & Benefits
Ordering Info
Touch for a solution

## Slide 3
4 Analog Channels
Auto attenuation and power for active probes
2 * USB HOST
Keyboard mouse and USB memory devices
MSO/Logic analysis
16 digital channels
Probe Calibration Signal
3.3 V, 1 kHz Square wave
10.1’’ Touch Screen
Easy use
supports gestures
Front Panel
Quick Search/Navigate
Play, FFW, Replay capture data frames

## Slide 4
10 MHz IN/OUT
AUX OUT
EXT TRIG
VGA OUTPUT
LAN INTERFACE
(VXI-11, telnet, socket, web)
USB-DEVICE(USBTMC)
USB HOST
Rear Panel

## Slide 5
1 GHz
Bandwidth
5 GSa/s
Sample Rate
110,000
wfm/s
Waveform Capture Rate
250 Mpts
Record Length
10.1’’
Touch Screen
LESS PRICE & MORE Power

## Slide 6
Bandwidth
Chart: SDS5104X -3dB Frequency Response
| 0.05 | 21 | 52 | 74 | 98 | 121 | 168 | 201 | 251 | 301 | 351 | 401 | 451 | 501 | 601 | 701 | 801 | 901 | 1001 | 1201 | 1401 | 1601
1 | 0 | 0 | -0.12379 | -0.082331 | -0.12379 | -0.16545 | -0.041068 | -0.041068 | 0.081558 | 0.081558 | 0.081558 | 0 | -0.12379 | -0.16545 | -0.12379 | -0.3768 | -0.59341 | -0.63739 | -1.4697 | -5.7782 | -11.051 | -17.6458
2 | 0 | 0 | -0.12379 | -0.082331 | -0.12379 | -0.16545 | 0 | 0 | 0.081558 | 0.12205 | 0.081558 | -0.082331 | -0.16545 | -0.24937 | -0.29164 | -0.4628 | -0.63739 | -0.63739 | -1.5673 | -5.6203 | -10.2285 | -16.9266
3 | 0 | 0.041068 | -0.082723 | -0.082723 | -0.12438 | -0.16624 | -0.041263 | -0.082723 | 0.041068 | 0.041068 | 0 | -0.16624 | -0.29305 | -0.37862 | -0.33573 | -0.42173 | -0.37862 | -0.37862 | -1.5262 | -6.4856 | -12.3172 | -19.6768
4 | 0 | 0 | -0.12438 | -0.082723 | -0.16624 | -0.16624 | -0.082723 | -0.041263 | 0.041068 | 0.081943 | 0.041068 | -0.082723 | -0.2083 | -0.33573 | -0.33573 | -0.59632 | -0.7745 | -0.72961 | -1.5754 | -5.6578 | -10.5403 | -17.0892
Increased accuracy for fast rise-time pulses and complex waveforms
Precisely reproduce waveforms with high frequency components

## Slide 7
Waveform Capture Rate
Up to 480,000 wfm/s (Sequence mode)
Collect measurement data more quickly
Up to 110,000 wfm/s (Normal mode)
Higher Capture Rate
Shorter Dead Time
Quickly identify problems = Faster results
Long dead time
Dead time
Dead time
You miss the glitch!!

## Slide 8
Color temperature display
Color and intensity Display
256-level intensity
More frequent events are brighter, or “hotter” (color display mode)
Significantly increase the probability of observing intermittent and elusive events
Reveal dynamic signal behavior

## Slide 9
250 Mpts Record Length
Hardware-based Zoom function
Benefits: Capture more of signal and zoom in areas of interest
Don’t lose horizontal resolution, don’t miss short intermittent signals.
Monitor slow signals with high sample rate.. Capture seconds of data and still have resolution to see nanosecond scale details
CH1 & CH2 share 250 Mpts memory
CH3 & CH4 share 250 Mpts memory

## Slide 10
Digital Trigger System
SDS5000X Digital Trigger
Analog Trigger
Trigger the same 25 MHz Sine wave
Unique digital trigger system: higher trigger sensitivity, lower trigger jitter (less than 100 ps)

## Slide 11
Intelligent Triggers
Setup
Featuring Qualified and Zone Trigger
Hardware trigger: Faster, less jitter
Multiple trigger types
Trigger source analog + digital channels + Other
Hold off by Events or Time

## Slide 12
Trigger on the first Rising Edge after 1ms High State
State
State with Delay
Edge
Edge with Delay
1ms
Qualified Trigger

## Slide 13
Zone Trigger
High waveform capture rate
allows you to see the anomaly
Once you see a glitch, draw a Zone Trigger box to locate it
Zone trigger easily isolates it without complicated traditional trigger settings.
Draw a zone trigger box to see the details

## Slide 14
Protocol
I2C, SPI Embedded serial trigger and analyze
UART Computer serial trigger and analyze
CAN, CAN FD, LIN Automotive serial trigger and analyze
FlexRay serial trigger and analyze
I2S Audio serial trigger and analyze
MIL-STD 1553B serial trigger and analyze
Format
Binary
Decimal
Hex
ASCII
Serial Bus Trigger and Decode
Trigger source: 2/4 analog + 16 digital channels
Event List

## Slide 15
Analog Front End
Extremely low back ground noise
Vertical scale full bandwidth 500μV/div-10V/div
Benefits
High SNR increase the ability to identify a small signal from the noise

## Slide 16
Sequence
Sequence N
Sequence N-1
Sequence N+1
Long Interval between two signals
Only save interested part
In Sequence mode, the dead time is only 1/5 of normal mode. Increasing the probability to capture anomalies.

## Slide 17
60S
60S
Capture long interval important signals and leave out idle time
Time stamp of each segment to analyze the frequency of the event.
ΔT = 60s
Sequence
Combine with History

## Slide 18
Running in background
Maximum records 100,000 frames
History
Navigation between frames

## Slide 19
Measurement
38 kinds of measurements
Gate
Measurement
Histogram
Vertical: Amplitude values, Mean&Stdev&RMS calculations , Overshoot parameters, Level measured at trigger position
Horizontal: Period, Frequency, Time difference between edges, Rise/Fall time, Duty, Delay,
Difference between two continuous periods
CH Delay: Phase difference, Time interval between two channels edges, Skew
Display 5 measurement statistics simultaneously
38 automatic measurements
Gate measurement by cursors supported
Measure on analog and digital channels, zoom, math, and Ref

## Slide 20
Jitter Measurement
Histogram to indicate the noise distribution
Measure the jitter of a 10.001 MHz signal generated by DDS technology.
Simple steps: Trigger, Zoom, Measure

## Slide 21
MATH
GATE INTEGRAL
View a differential signal without differential probe
Power Calculations (P = IV onscreen)
Integrate power to calculate energy
Ratio of amplified signals

## Slide 22
2Mpts FFT
Edit Center Freq and division with pop-up keyboard easily
High calculation speed
Five types of Windows
Normal, Max-Hold, Average
FFT mode
Extremely high FFT resolution
The frequency resolution depends on the
sampling rate and the number of FFT points
(fs/N).

## Slide 23
MATH on MATH
Measure the instant power on a MOSFET without a differential probe
P = VDS * ID
CH1 = VD, CH2 = VS, CH3 = ID, CH4 = VG, P = (CH1 – CH2) * CH3
Use a differential probe to measure VDS then perform an integral on power to calculate the energy generated when MOSFET is powered on

## Slide 24
Search and Navigate
Set up search criteria
Find and mark events you are interested within one second
One Key Navigate – Elements that match search are marked with a white arrow for easy identification.

## Slide 25
DVM & Frequency Counter
Built-in standard 4-digit digital voltmeter
Support Auto Range, Bar, Trend, Histogram
The same probe as the oscilloscope channels
DVM measurements and scope acquisition are independent
7-digit frequency counter with bandwidth up to 1 GHz, useful in many high frequency applications

## Slide 26
Waveform Histogram
Draw a box to locate area of interest
See the vertical and horizontal signal value changes

## Slide 27
Eres Mode
Eres Mode
Enhance SNR by decreasing BW of
noise via digital filter
Improve ENOB (Effective number of
bits) by 3 Bit at most. Means
enhancement of vertical resolution
Independent on signal period and stability
of trigger point

## Slide 28
MASK TEST
High speed Pass/Fail test
Customize template, specified standards in manufacturing
Automatic test environment: stop acquiring, beep alert, 3.3V
TTL output as external source (Pass/Fail out)
Implemented by hardware, test rate up to
110,000 times/s
Functional MASK EDITOR with touch screen
Create MASK point-by-point
Input coordinates by touch screen
Draw polygon on screen
Easy to save and load mask files

## Slide 29
Easy Of Use
10.1’’ Touch Screen
Multi -Touch
10 kinds of one button quick access
Default
Measure
Clear
Cursors
Display
Print
History
Navigate
Search
Auto
1024 * 600
Easy to learn, gesture support
Four ways to control scope:
Touch screen like your smart phone
Front panel buttons and knobs for traditional users
USB Keyboard and Mouse support
Web server for remote control
Focus on your design, but not instruments
Increase work efficiency and productivity

## Slide 30
Ease-Of-Use
10 kinds of one button quick access
Four ways to control scope:
Touch screen like your smart phone
Front panel buttons and knobs for traditional users
USB Keyboard and Mouse support
Web server for remote control
Focus on your design, but not instruments
Increase work efficiency and productivity
Easy to learn, gesture support
Deep on-board Help for quick access to information:

## Slide 31
Web Server
Remote control scope without software
Save time to export measurement data to PC
Monitor and control SDS5000X from anywhere via the internet
Insert IP address of SDS5000X into browser
Go to Home page see the SDS5000X info
Control scope via mouse in real time
Take screen shot , save data and FW upgrade

## Slide 32
View digital and analog channels on one timebase
Full trigger and decoding on all analog and digital channels
16 channels; maximum waveform capture rate up to 1.25GSa/s; record length up to 62.5 Mpts
User defined label names, channel groups, and more
16 Digital Channels / MSO (Option)

## Slide 33
Connect via USB Host
Stimulus output of Sine, Square, Ramp, Pulse, Noise, DC and 45 built-in waveforms to DUT
Edit arbitrary waveforms via Easy Wave PC software
Store waveforms from analog channels then output
25 MHz Function/Arbitrary
Waveform Generator
(Option)

## Slide 34
SDS5000X Models | SDS5034X SDS5032X | SDS5054X SDS5052X | SDS5104X SDS5102X
Bandwidth | 350 MHz | 500 MHz | 1 GHz
Rise time (typical) @50 Ω | 1.0 ns | 0.7 ns | 0.4 ns
Analog Channels | 2/4 CH + EXT |  | 
Sample Rate (Max.) | 5G Sa/s (single-channel),2.5G Sa/s (dual-channel) |  | 
Record Length (Max.) | 250 Mpts (single-channel),125 Mpts (dual-channel) |  | 
Waveform Capture Rate (Max.) | 110,000 wfm/s (normal mode),480,000 wfm/s (sequence mode) |  | 
Trigger Types | Edge, Slope, Pulse, Window, Runt, Interval, Dropout, Pattern, Qualified, Video, Zone |  | 
Serial Trigger and Decode | I2C, SPI, UART, CAN, LIN, CAN FD, FlexRay, MIL 1553B, I2S |  | 
I/O | USB Host, USB Device, LAN, Pass/Fail, Trigger Out, 10 MHz In,10 MHz Out, VGA Output |  | 
Probe (standard) | SP2035A: 350 MHz or SP3050A: 500 MHz 1 probe supplied for each channel |  | 
Display | 10.1” TFT-LCD with capacitive touch screen(1024*600) |  | 
Model Selection

## Slide 35
The reason to Choose SDS5000X
Touch for a solution
Flat frequency response curve
High waveform capture: Quickly identify problems
Color display: Reveal dynamic signal behavior
Large memory: Capture seconds of data and still have
resolution to see nanosecond scale details
Digital trigger: Higher trigger sensitivity, lower trigger jitter
Hardware intelligent trigger: Faster, less jitter
Zone trigger: Draw a box to locate interested signals
Multiple serial protocols trigger and decode
Extremely low back ground noise
Standard Sequence, History, Search, Navigate
Measurement with Histogram; Jitter measurement
Math on Math, 2 Mpts FFT
Standard DVM & Frequency Counter
Eres Mode: Improve resolution up to 11 bits
Mask test and Mask creator with touch screen
Quick access Help
Web control
16 digital channels
25 MHz function generator

## Slide 36
 | Standard Accessories
 | USB cable*1
 | Quick start*1
 | Passive probe*2 (2-ch model); *4(4-ch model) SP2035A: 350 MHz or SP3050A: 500 MHz
 | Certificate of calibration*1
 | Power cord*1
Ordering information
Optional Accessories | Description
SDS-5000X-BW05 SDS-5000X-BW10 | 350 MHz to 500 MHz bandwidth upgrade 500 MHz to 1 GHz bandwidth upgrade
SDS-5000X-FG | Waveform generator software
SAG1021 | 25 MHz USB function/arbitrary waveform generator
SDS-5000X-16LA | 16 digital channels (software)
SPL2016 | 16-channel logic probe
STB3 | STB3 demo signal source
SAP1000 | 1 GHz active probe
HPB4010 | High voltage probe
CP4020/CP4050/CP4070/ CP4070A/ CP5030/ CP5030A/CP5150/CP5500 | Current probe
DPB4080/DPB5150/ DPB5150A/ DPB5700/ DPB5700A | High voltage differential probe
SDS-5000X-I2S | I2S trigger & decode
SDS-5000X-CANFD | CAN FD trigger & decode
SDS-5000X-FlexRay | FlexRay trigger & decode
SDS-5000X-1553B | MIL-STD-1553B trigger & decode

## Slide 37
Company Address
Building No.4 & No.5，Antongda Industrial Zone，3rd Liuxian Road,Bao’an District, Shenzhen, China
Contact Info
www.siglent.com/ens
Email：sales@siglent.com
Tel：+86-755-36615186
SIGLENT—The Best Value in Electronic Test & Measurement
Thank You