## Slide 1
The Best Value in Electronic Test & Measurement

## Slide 2
SSG3000X Series
RF Signal Generators

## Slide 3
Overview
Panel Introduction
Key Features
Product Comparison
Contents

## Slide 4
Overview
Section 1

## Slide 5
Frequency range from 9 kHz to 2.1 / 3.2 GHz
0.01 Hz minimum frequency setpoint resolution
Level output from to -110 dBm to +13 dBm
Maximum level up to 20 dBm (Typical)
Minimum amplitude resolution as low as 0.01 dB
Internal modulation includes AM/FM/PM, external modulation as well
Pulse modulation, on/off ratio ≥ 70 dBc
Pulse train generator (Option) , user-definable pulse sequence
Power meter measurement kit, easy to measure power and control the output
Communication interfaces: USB Host, USB Device (USBTMC), GPIB (option)
Web browser remote control
5-inch capacitive touch screen, USB mouse/keyboard support
Overview
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 6
Frequency sweep, amplitude sweep,
Frequency + amplitude sweep
Overview
PULSE
AM
LF
CW
SENSOR
SWEEP
Sine、Square、 DC、triangle, saw-tooth
9 kHz -- 3.2 GHz
+13 dBm-- -110 dBm
USB power meter corrects flatness to keep power constant
I/Q
PULSE
FM/PM
Internal/External Modulation
Internal and external modulation customization
Pulse train generator
Digital Modulation
Internal/External Modulation
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 7
Key Features
Section 2

## Slide 8
Key Features
Maximum frequency up-to 3.2 GHz
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 9
Key Features
Maximum level up to 20 dBm
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 10
Key Features
High purity signal output
Phase noise ＜ -110 dBc/Hz @ 1 GHz , 20 kHz offset (Typical)
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 11
Key Features
FM/AM/PM/Pulse Modulation
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 12
Pulse Generator
Pulse Modulation
Pulse In/Out
Pulse Train Generator
RF output
ΦM Modulation
Internal Analog Modulation Source
External Modulation Signal Input
AM Modulation
FM Modulation
LF Output
Key Features
Analog & Pulse Modulation
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 13
Key Features
Double Pulse Modulation
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 14
Key Features
Pulse Train Modulation
Maximum up-to 2047 pulses
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 15
Key Features
Digital Modulation
Easy IQ
Digital Source Editor
Digital Modulation
Pulse Shaping Filter
I / Q Baseband Generator
I/Q Modulation
SDG6000X
External IQ Baseband Generator
SSG3000X
I/Q Modulation
RF Output
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 16
Key Features
I/Q modulation signal output
Using a SIGLENT SDG6000X function generator, I/Q modulation can be realized by using the SSG3000X external modulation function
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 17
Key Features
USB-power meter reading display
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 18
Key Features
Web page control
Directly control the SSG3000X by browser interface. No driver or additional software required
Notes: 输出频率分辨率可达0.01Hz
输出范围可从+13dBm~-115dBm
最大输出功率可达20dBm(典型值)
幅度最小分辨率可达0.01dB

## Slide 19
Panel Introduction
Front Panel
Rear Panel
Section 3

## Slide 20
Front Panel
Function keys
Main On/Off
Arrow keys
Knob
Number keypad
Display
RF output
LF output
Function
On/Off

## Slide 21
Rear Panel
Trig In/Out
Pulse In/Out
10 MHz In
USB Device
LAN Interface
Power Interface
USB Interface
EXT MOD INPUT
10 MHz Clock Out
Signal
Valid
Out
I Input
Q Input

## Slide 22
Competitive
Comparison
Section 4

## Slide 23
Comparison
Para/Model | SIGLENT SSG3000X | Keysight N9310A | R&S SMC100A | Rigol DSG3030 | Rigol DSG800
Appearance |  |  |  |  | 
Frequency Range | 9 kHz – 3.2 GHz | 9 kHz – 3.0 GHz | 9 kHz – 3.2 GHz | 9 kHz – 3.0 GHz | 9 kHz – 3.0 GHz
Frequency Resolution | 0.01 Hz | 0.1 Hz | 0.001 Hz | 0.01 Hz | 0.01 Hz
Temperature stability | 1 ppm | 1 ppm | 2 ppm | 0.5 ppm | 2 ppm
Amplitude Dynamic Range | -110 dBm - +13 dBm | -127 dBm - +13 dBm | -120 dBm - +13 dBm | -130 dBm - +13 dBm | -110 dBm - +13 dBm
Maximum output power | 20 dBm | 20 dBm | 17 dBm | 25 dBm | 20 dBm
Full amplitude accuracy | < 0.7 dB | < 1 dB | < 0.9 dB | < 0.7 dB | < 0.7 dB
Phase Noise@1GHz （20Khz offset） | -110 dBc/Hz | -95 dBc/Hz | -111 dBc/Hz | -110 dBc/Hz | -105 dBc/Hz
Frequency switch switching time | < 10 ms | < 10 ms | < 7 ms | < 10 ms | < 10 ms
harmonic (1MHz<f<3.2GHz) | < -30 dBc | < -30 dBc | < -30 dBc | < -30 dBc | < -30 dBc
Non-harmonic | < -65 dBc | < -50 dBc | < -54 dBc | < -64 dBc | < -64 dBc
AM/FM/PM Modulation | Supported | Supported | Supported | Supported | Supported

## Slide 24
Para/Model | SIGLENT SSG3000X | Keysight N9310A | R&S SMC100A | Rigol DSG3030 | Rigol DSG800
Appearance |  |  |  |  | 
Pulse Modulation | Standard | Standard | Standard | Standard | Option
Pulse on/off ratio | >70 dB | >40 dB | >80 dB | >80 dB | >70 dB
Pulse Generator | Standard | Not support | Standard | Standard | Option
Pulse Burst | Supported | Not Supported | Not Supported | Supported | Supported
Power meter measurement and control | Standard | Not Supported | Standard | Standard | Not Supported
IQ Modulation | Supported | Supported | Supported | Supported | Supported
Memory | 256 MB | 16 MB | ---- | 1 GB | 96 MB
Web server | Supported | Not Supported | Not Supported | Not Supported | Not Supported
Interface | USB Host/Device, LAN, GPIB(Option) | USB Host, USB Device | USB Host, USB Device, LAN | USB Host/Device, LAN, GPIB | USB Host/Device, LAN
Mouse and keyboard | Supported | Not Supported | Supported | Not Supported | Not Supported
Touch screen | Capacitive touch screen | Not Supported | Not Supported | Not Supported | Not Supported
Display | 5 inch TFT-LCD（800*480） | LCD 640*480 | LCD display | 4.3 inch TFT-LCD（480*272） | 3.5 inch TFT-LCD（320*240）
Comparison

## Slide 25
Company Address
Bldg No.4 & No.5，
Antongda Industrial Zone
3rd Liuxian Road, Bao’an District, Shenzhen, China
Contact Info
www.siglent.com/ens
Email：sales@siglent.com
Tel：+86-755-36887876
SIGLENT—The Best Value in Electronic Test & Measurement
Thank You