## Slide 3
3
Capture any signal with precision and confidence
Measurement accuracy comparable to performance benchtop instruments.
Conduct proficient testing in complex environments
Lightweight, portable, durable, specially designed for field operation.
Utilize portable analyzer functions
Cable and antenna analyzer (CAT)
Vector network analyzer (VNA)
Spectrum analyzer (SA)
Provide budget flexibility
Select the current required features and easily upgrade in the future to advance with changing measurement requirements.
01
02
03
04
Why should you choose SHA850A?
Multifunction Handheld Spectrum Analyzer

## Slide 4
Traditional measurement technology of SIGLENT
Innovation brought by SHA850A
2019.09
SSA3000X Plus Spectrum Analyzer
2019.09
SVA1000X Spectrum & Vector Network Analyzer
2020.04
SSA3000X-R Real-time Spectrum Analyzer
2022.09
SSA5000A Spectrum Analyzer
2023.05
Cable and antenna analyzer
DTF and SWR measurement
Vector network analyzer
Dynamic range up to 114 dB
Spectrum analyzer
± 0.7 dB Total amplitude accuracy
4

## Slide 5
Outstanding Characteristics
Subtle Design
Multiple Functions
Spectrum Analyzer
Vector Network Analyzer
Cable and Antenna Test
Analog Modulation Analysis
Digital Modulation Analysis
···
Small size
Touch screen
Abundant communication interface
Intuitive operation interface
···
Wide dynamic range
Low phase noise
Independent source
Standard preamplifier
···
5

## Slide 6
Basic Info
Market and Application
Features and Benefits
Competition Analysis
Contents

## Slide 7
Specification
7
Model | SHA851A | SHA852A
Spectrum Analyzer | 9 kHz ~ 3.6 GHz | 9 kHz ~ 7.5 GHz
Vector Network Analyzer (SHA850-VNA) | 100 kHz ~ 3.6 GHz | 100 kHz ~ 7.5 GHz
Cable and Antenna Test | 100 kHz ~ 3.6 GHz | 100 kHz ~ 7.5 GHz
Source | 100 kHz ~ 3.6/7.5 GHz (option SHA850-SOR) | 
Preamplifier | 25 dB, standard | 
Displayed Average Noise Level | -165 dBm (typ.), Preamp on, best, 20 °C to 30 °C | 
SSB Phase Noise | -104 dBc/Hz (typ.) @ fc = 1 GHz, Offset 10 kHz | 
Dynamic Range | 114 dB | 
Advanced Measurement Kit | CHP, Channel Power; ACPR, Adjacent Channel Power Ratio; OBW, Occupied Bandwidth; T-Power, Time Domain Power; CNR, Carrier Noise Ratio; Harmonic measurement; TOI, Third-Order Intercept; Spectrogram(option SHA850-AMK) | 
Analog Modulation Analysis | AM, FM, PM (option SHA850-AMA) | 
Digital Modulation Analysis | ASK: 2ASK; FSK: 2FSK, 4FSK, 8FSK, 16FSK;MSK: GMSK;PSK: BPSK, QPSK, OQPSK, 8PSK; DPSK: DBPSK, DQPSK, D8PSK, π/4 -DQPSK, π/8 -D8PSK; QAM: 16, 32, 64, 128, 256(option SHA850-DMA) | 
Dimensions | 310 mm × 215 mm × 78.5 mm (W×H×D) | 
Operating time | 4h | 

## Slide 8
Features and Benefits
make operation more fluent.
8
01
8.4" touch screen
Simple UI interface
Easy to use
02
Abundant communication interfaces
Support mouse and remote web page control
More connection and control modes
04
Sources
Option SHA850-SOR
Transmission response of filter
Cable insertion loss
06
VNA
Option SHA850-VNA
Amplitude and phase parameters
03
Low phase noise -104 dBc/Hz
Provides excellent signal quality
Excellent phase performance
05
High performance RF components
Improve accuracy and stability of the measurement results
Less trace noise

## Slide 9
High dynamic range 114 dB
It can be applied to test scenes that require high dynamic range, such as measuring the passband and out-of-band suppression performance of filters at the same time, and measuring narrow-band devices with high suppression, such as cavity filters.
Ecal
Shorten the calibration time and reduce the number of connections in the test, while providing higher measurement consistency, less human error and higher accuracy.
Advanced measurement kit
A variety of intelligent measurement functions are integrated into a portable instrument powered by battery, which can easily complete the measurement task.
GPS option
Provide geographical location labels for measurement, and geographical data such as longitude, latitude and altitude can be displayed on the screen and saved in data files.
Bias Out
Power supply for external offset connectors, probes and active devices saves time and improves measurement accuracy.
9

## Slide 10
310.1 mm
LCD Screen
Menu
Multifunction knob
Measurement control, Pause or resume the current measurement process
Shortcut screenshot button
Key and touch screen lock control
Reuse keys for menu selection mode and numerical input mode, which can be switched by Enter and Esc.
10
Front Panel
Notes: Large horizontal screen design and large buttons for easy operation and observation-you can operate with gloves on.
Multifunction knob
complete the rapid adjustment and selection of parameters.
Key and touch screen lock control
Turn off or turn on keyboard and touch functions to prevent misoperation.

## Slide 11
Logo
Hardware
Measurement status bar
Result display area
Scan parameter area
Menu area
Mode/Measure
11
User Interface
Left
Fan vent
Battery case cover
215mm

## Slide 12
The connector recess can protect the RF connector well.
Audio output
3.5 mm
USB Host
USB Device
Built-in DC power supply can supply power for external bias connectors, probes and active devices, SMB female
Built-in GPS receiver provides accurate position information, SMA female
Hand strap buckle
External trigger signal input
External reference signal
LAN
Independent source
RF In/Port 2
External power supply
K groove
78.5 mm
12
Rear Panel

## Slide 13
Basic Info
Market and Application
Features and Benefits
Competition Analysis
Contents

## Slide 14
14
Any signal. Anytime. Anywhere.
Design Features
8.4 inch multi-touch screen
Quickly adjust waveform
Easily activate features and settings
Improve operation efficiency
Support network remote control
…

## Slide 15
15
Any signal. Anytime. Anywhere.
GPS
Area for "GPS display information“
Area for "GPS satellite lock icon“
GPS display information:
Fix: Invalid / Estimated: Unknown system /
GNSS: global navigation satellite system /
DGPS: differential global positioning system
Satellite: number of Satellites
Latitude
Longitude
Altitude
*Requires GPS Antenna and GPS Receiver Option. GPS Logging Option for saving data.

## Slide 16
16
Any signal. Anytime. Anywhere.
Low DANL
-165 dBm/Hz
Low noise
High performance RF design
Provide standard built-in preamplifier
Improving weak signal monitoring with high sensitivity

## Slide 17
17
Any signal. Anytime. Anywhere.
Low Phase Noise
-104 dBc/Hz
A measurement parameter of the frequency stability of the oscillator
An important index for evaluating spectrum analyzers – SHA800A has better performance than SSA3000X-R series

## Slide 18
18
Any signal. Anytime. Anywhere.
ACPR
Common measurement characteristic for channel-based communication protocols.
It can describe the out-of-band spectrum distortion characteristics of signal caused by nonlinear distortion of power amplifier
*Requires AMK (Advanced Measurement Kit) Option

## Slide 19
19
Any signal. Anytime. Anywhere.
Harmonic Analysis
Measure the harmonic power and total harmonic distortion of carrier signal
The maximum measurable harmonic is the 10th harmonic
The fundamental amplitude of the carrier signal should be greater than -50 dBm
*Requires AMK (Advanced Measurement Kit) Option

## Slide 20
20
Any signal. Anytime. Anywhere.
TOI
IP3: Third-order Intercept Point
An important index to measure linearity or distortion of amplifiers, mixers, and receivers
*Requires AMK (Advanced Measurement Kit) Option

## Slide 21
21
Any signal. Anytime. Anywhere.
Spectrum Monitor
Color represents spectral energy
The X axis is frequency
The Y axis is time
Also called Spectrogram or Waterfall Chart
By detecting the non-continuous and frequency hopping signals
We can observe the change of the signal over a longer period of time
*Requires AMK (Advanced Measurement Kit) Option

## Slide 22
22
Any signal. Anytime. Anywhere.
Signal Modulation Analysis
Analog signal: AM/FM/PM (AMA Option)
Digital signal: ASK/FSK/PSK/QAM (DMA Option)
EVM (Error Vector Magnitude) Calculation
Transmission quality factors
Visualization modes include eye-diagrams and constellations
Extends troubleshooting to complex signals and systems
*Requires AMA / DMA Option

## Slide 23
23
Any signal. Anytime. Anywhere.
Digital Modulation Analysis
Display in binary or hexadecimal
Compare captured data to known data to calculate BER (Bit Error Rate)
*Requires DMA Option

## Slide 24
24
Any signal. Anytime. Anywhere.
DTF
Detecting Cable Quality
Service Maintenance
Performance Verification
Fault Analysis
*Standard in CAT mode

## Slide 25
25
Any signal. Anytime. Anywhere.
VNA
Easily measure S11 and S21
10001 maximum measuring points
The display contents include:
Simultaneous S11 and S21 display provides simple and intuitive impedance measurements
Phase
Group Delay
Polar Chart
Smith Chart
…
*Requires VNA Option

## Slide 26
26
Any signal. Anytime. Anywhere.
SWR
An index indicating the matching degree between antenna and base station
Ideal VSWR = 1. The greater the VSWR, the greater the reflection and therefore, the worse worse the match
*Available in VNA mode Option
Notes: Better signal fidelity than CAT mode

## Slide 27
27
Any signal. Anytime. Anywhere.
Insertion Loss/Return Loss
Insertion loss can represent the loss of jumper cable, feeder cable, duplexer, etc.
Or the gain of tower top amplifier
Return loss (RL) is an important parameter for measuring and verifying cable and antenna systems
The measurement results can reflect the power transmission efficiency of the system
*Requires VNA Option
Notes: Better signal fidelity than CAT mode

## Slide 28
28
Any signal. Anytime. Anywhere.
Port Extension
Eliminates the error of test fixture
The reference plane can be extended to the specified measurement plane so that more accurate testing can be carried out
*Requires VNA Option

## Slide 29
29
Any signal. Anytime. Anywhere.
Ecal
Supports user calibration kit
Shortens the calibration time
Reduces the number of connections
Provides higher measurement consistency
Reduces human error and improves accuracy
*Requires VNA Option

## Slide 30
Basic Info
Market and Application
Features and Benefits
Competition Analysis
Contents

## Slide 31
31
Device parameter Verification
Measure the characteristics of amplifiers, mixers, filters and other devices in the field
Test the performance, bandwidth, intermodulation distortion and many other indicators
Site Installation & Troubleshooting
Site survey
Radio link installation
Site acceptance
Design and assembly troubleshooting
Failure Analysis in the field
Characterize RF devices
Characterize electronic components including
Resistors, Capacitors, Inductors…
Filters, Cables, Mixers, Connectors…
Antennas, Amplifiers, Attenuators…
Any signal. Anytime. Anywhere.
Market and Application
Comparative measurement of received signal power
Fast location of interference signals
Installation and maintenance of base station
Cable and antenna measurement
Wireless equipment field test
Field strength coverage measurement
Telecom drive test operation and maintenance
Communication Engineering

## Slide 32
32
Fault diagnosis and maintenance to ensure the continuity of communication.
Most microwave link equipment problems are related to cables, antennas and connectors.
If the performance of the feeder is degraded, it may lead to problems such as
Telecom drive test operation and maintenance
Installation and maintenance of cellular systems
Reduced coverage
Link failure
Decreased sensitivity of the receiver path

## Slide 33
In applications such as communication and commercial microwave backhaul
Hardware installation and maintenance
Detecting the quality of wireless signals
Periodically detect unexpected signals
Signal monitoring
Example
Detecting low-level signals or neighboring small interference signals under strong signal conditions requires high dynamic range.
While the latter requires excellent phase noise performance.
Radio Monitoring
Management
33

## Slide 34
34
Verify station parameters including frequency and power
Debug cables and connections
Characterize active and passive devices including amplifiers and antennas
Conduct on-site verification and followup
Station Installation
Verification

## Slide 35
Basic Info
Market and Application
Features and Benefits
Competition Analysis
Contents

## Slide 36
Model | SIGLENT SHA850A | KEYSIGHT N9913/4A | R&S ZPH | Anritsu MS2034/5B
Appearance |  |  |  | 
Spectrum Analyzer | 9 kHz ~ 3.6/7.5 GHz | 5 kHz ~ 4 GHz/6.5 GHz(option 233) | 5 kHz ~ 3 GHz/4 GHz(option ZPH-B4) | 9 kHz ~ 4/6 GHz
Vector Network Analyzer | 100 kHz ~ 3.6/7.5 GHz (option SHA850-VNA) | 30 kHz to 4/6.5 GHz (N9914A-V5K) (N9914A-210; N9914A-211) | 2 MHz to 3 GHz/4 GHz (option ZPH-B4) | 500 kHz ~ 4/6 GHz
Cable and Antenna Analyzer | 100 kHz ~ 3.6/7.5 GHz | 30 kHz to 4/6.5 GHz (N9914A-V5K: 5kHz start frequency) | 2 MHz to 3 GHz/4 GHz (option ZPH-B4) | 500 kHz ~ 4/6 GHz
DANL | -165 dBm/Hz | -155 dBm/Hz | -163 dBm/Hz | -162 dBm
SSB Phase Noise | fc = 1 GH, offset 10 kHz -104 dBc/Hz (typ.) | fc = 1 GH, offset 10 kHz -111 dBc/Hz(typ.) | fc = 500 MHz, offset 30 kHz -95 dBc/Hz(typ.) | fc = 1 GH, offset 10 kHz –110 dBc/Hz(typ.)
Dynamic Range (typ.) | 114 dB | 100 dB | > 90 dB | 100 dB
Analog Modulation Analysis | AM/FM/PM (option SHA850-AMA) | AM/FM (Option 355) | AM/FM (option ZPH-K7) | AM/FM/PM (Option 509)
Digital Modulation Analysis | ASK/FSK/MSK/PSK/DPSK/QAM (option SHA850-DMA) | none | none | none
Measurement range | DANL to +10 dBm, 100 kHz ~ 1 MHz DANL to +20 dBm, 1 MHz ~ 7.5 GHz | DANL to +20 dBm | DANL to +30 dBm | DANL to +26 dBm (≥ 50 MHz) DANL to 0 dBm (< 50 MHz)
Preamplifier | 25 dB (nom.), standard | +20 dB (Option 235) | option | standard
Source | 100 kHz ~ 3.6/7.5 GHz (option SHA850-SOR) | 30 kHz to 4/6.5 GHz | 100 kHz ~ 4 GHz | unspecified
Dimensions | 310.1 x 215 x 78.5 mm | 292 x 188 x 72 mm | 294 x 202 x 76 mm | 273 x 199 x 91 mm
Operating time | 4 hours | 3.5 hours | 6.5 ~ 9 hours | 3.6 hours
36

## Slide 37
Model | SIGLENT SHA850A | KEYSIGHT N9912A | R&S FPH | Anritsu MS2080A
Appearance |  |  |  | 
Spectrum Analyzer | 9 kHz ~ 3.6/7.5 GHz | N9912AU-230: 100 kHz to 4 GHz N9912AU-231: 100 kHz to 6 GHz | 5 kHz to 2 GHz(model .02) 5 kHz to 6 GHz(model .06) | 9 kHz ~ 4 GHz (Option 704)
Vector Network Analyzer | 100 kHz ~ 3.6/7.5 GHz (option SHA850-VNA) | Option 104:2 MHz to 4 GHz Option 106:2 MHz to 6 GHz (S11 – Option 303; S21 – Option 110 and 303) | none | none
Cable and Antenna Analyzer | 100 kHz ~ 3.6/7.5 GHz | Option 104: 2 MHz to 4 GHz Option 106: 2 MHz to 6 GHz | none | 150 kHz to 4 GHz (S331P-0704) 150 kHz to 6 GHz (S331P-0706)
DANL | -165 dBm/Hz | -148 dBm/Hz | -163 dBm/Hz | -167 dBm
SSB Phase Noise | fc = 1 GH, offset 10 kHz -104 dBc/Hz (typ.) | fc = 1 GH, offset 10 kHz -88 dBc/Hz(typ.) | fc = 500 MHz, offset 30 kHz -95 dBc/Hz(typ.) | fc = 1 GH, offset 10 kHz –94 dBc/Hz(typ.)
Dynamic Range (typ.) | 114 dB | unspecified | none | >105 dB Typical
Analog Modulation Analysis | AM/FM/PM (option SHA850-AMA) | AM/FM (Option 230 or 231) | AM/FM (option FPH-K7) | AM/FM (Option 24)
Digital Modulation Analysis | ASK/FSK/MSK/PSK/DPSK/QAM (option SHA850-DMA) | none | ASK/FSK (option FPH-K7) | none
Measurement range | DANL to +10 dBm, 100 kHz ~ 1 MHz DANL to +20 dBm, 1 MHz ~ 7.5 GHz | DANL to +20 dBm | DANL to +30 dBm | DANL to +30 dBm
Preamplifier | 25 dB (nom.), standard | +22 dB (Option 235) | option | standard
Source | 100 kHz ~ 3.6/7.5 GHz (option SHA850-SOR) | N9912AU-230: 2 MHz to 4 GHz N9912AU-231: 2 MHz to 6 GHz | 100 kHz to MAX frequency | unspecified
Dimensions | 310.1 x 215 x 78.5 mm | 292 x 188 x 72 mm | 294 x 202 x 76 mm | 290 x 212 x 96 mm
Operating time | 4 hours | 4 hours (typical) | 8 h(model .02) / 7 h(model .06) | 3 h with Internal 6 h with Accessory Power Pack
37

## Slide 38
38
S5000 Directional Antenna Set
Model | ANT-DA13 (S5001-LP) | ANT-DA12 (S5001-UHF) | ANT-DA11 (S5001-VHF)
Frequency Range | 500MHz-8GHz | 200MHz – 500MHz | 10MHz – 200MHz
Appearance |  |  | 
Antenna Gain | 10dB (typ.) |  | 
SWR | ＜1:1.9 (typ.) |  | 
Direction Of Polarization | horizontal, vertical |  | 
RF Interface | 50Ω/N type, female |  | 
Handle Radio Frequency Wire | 1.5m /N type, male |  | 
Handle Amplifier Gain | 12dB @1GHz, more than 50 hours |  | 
Dimensions | 470 x 400 x 240mm |  | 
Rough Weight | 4.8kg (including packing box) | 4.8kg (including packing box) | 4.8kg (including packing box)
Net Weight | 0.45kg (including handle 0.96kg) | 0.32kg (including handle 0.83kg) | 0.50kg (including handle 1.01kg)

## Slide 39
39
Pattern and application diagram

## Slide 40
40
Type | Model Name | Description | Price | Availability
Product Code | SHA851A | Spectrum & Vector Network Analyzer, 9 kHz~3.6 GHz | $4,860 | 4-6 weeks
 | SHA852A | Spectrum & Vector Network Analyzer, 9 kHz~7.5 GHz | $7,650 | 4-6 weeks
Options | SHA850-F2 | SHA851A to SHA852A | $4,022 | Stock
 | SHA850-SOR | Source | $297 | Stock
 | SHA850-VNA | Vector Network Analysis | $1,019 | Stock
 | SHA850-AMK | Advanced Measurement Kit | $400 | Stock
 | SHA850-AMA | Analog Modulation Analysis | $338 | Stock
 | SHA850-DMA | Digital Modulation Analysis | $606 | Stock
 | SHA850-BIAS | DC Bias Out | $132 | Stock
 | SHA850-GPS | GPS Receiver | $173 | Stock
 | SHA850-GPSM | GPS Logging(need GPS Receiver) | $173 | Stock
Antenna Accessories | ANT-GPS1 | GPS Antenna with male SMA connector | $20 | 4-6 weeks
 | ANT-DA1 | Contains amplifier handle and 3 antennas: 10-200 MHz, 200-500 MHz, and 500 MHz-8 GHz | $7,614 | 4-6 weeks
 | ANT-DA11 | Contains amplifier handle and 10MHz ~ 200MHz antenna | $3,080 | 4-6 weeks
 | ANT-DA12 | Contains amplifier handle and 200MHz ~ 500MHz antenna | $3,065 | 4-6 weeks
 | ANT-DA13 | Contains amplifier handle and 500MHz ~ 8GHz antenna | $3,673 | 4-6 weeks
Pricing & Availability

## Slide 41
41
Product | Description | Order Number
General Accessories | Rechargeable lithium battery | SHA800-BAT
 | AC-DC adapter | SHA800-AP
Options | Portable bag | SHA800-BG
 | GPS antenna, SMA(M), 100cm | ANT-GPS1
 | S5000 Directional Antenna Set: S5001-VHF(10 MHz~200 MHz), S5001-UHF(200 MHz~500 MHz), S5001-LP(500 MHz~8 GHz), Preamp(10 dB, 9 kHz~8 GHz) | ANT-DA1
 | Near field probe kit：300 kHz~3 GHz, H-field probes(20 mm,10 mm,5 mm), E-field probe(5 mm) | SRF5030T
 | Utility Kit: N(M)-SMA(M) cable(6 GHz), N(M)-N(M) cable(6 GHz), N(M)-BNC(F) adaptor x2, N(M)-SMA(F) adaptor x2, 10 dB 1W attenuator | UKitSSA3X
 | N(M)-BNC(M) cable, DC~2 GHz, 700 mm | N-BNC-2L
 | N(M)-SMA(M) cable, DC~6 GHz, 700 mm | N-SMA-6L
 | N(M)-N(M) cable, DC~6 GHz, 700 mm | N-N-6L
 | N(M)-N(M) cable ,DC~18 GHz，1000 mm | N-N-18L
CAT&VNA Accessories | N(M)-SMA(M) cable ,DC~18 GHz，1000 mm | N-SMA-18L
 | SMA(M)-SMA(M) cable ,DC~18 GHz，1000 mm | SMA-SMA-18L
General Accessories

## Slide 42
42
Model | Max Frequency | Most Popular Calibration Kit | Alternate Cal Kit for reverse gender | Complete Kit for both genders
SHA851A | 3.6 GHz | F503ME | F503FE | F504TS
SHA852A | 7.5 GHz | F504MS | F504FS | F504TS
VNA Calibration Kit Selection
F503ME
F504TS
Calibration Kit Model | Max Frequency | Calibration Kit Connectors | Calibration Kit Gender
F503FE | 4.5 GHz | N Type (F) | Female
F503ME | 4.5 GHz | N Type (M) | Male
F603FE | 4.5 GHz | 3.5 mm | Female
F603ME | 4.5 GHz | 3.5 mm | Male
F504FS | 9 GHz | N Type (F) | Female
F504MS | 9 GHz | N Type (M) | Male
F504TS | 9 GHz | N Type (M & F) | Male & Female w/ Wrench
F604FS | 9 GHz | 3.5 mm | Female
F604MS | 9 GHz | 3.5 mm | Male
F604TS | 9 GHz | 3.5 mm | Male & Female w/ Wrench
Y504FS | 9 GHz | N Type (F) | Female
Y504MS | 9 GHz | N Type (M) | Male

## Slide 43
SIGLENT TECHNOLOGIES GERMANY GmbH
Add: Staetzlinger Str. 70 86165 Augsburg, Germany Tel: +49(0)-821-666 0 111 0 Fax: +49(0)-821-666 0 111 22 info-eu@siglent.com www.siglenteu.com
NA
SIGLENT Technologies NA, Inc.
Add: 6557 Cochran Rd Solon, Ohio 44139 Tel: 440-398-5800 Toll Free:877-515-5551 Fax: 440-399-1211
info@siglent.com www.siglentna.com
Every Bench. Every Engineer. Every Day.
Thank You
Europe
SIGLENT TECHNOLOGIES CO., LTD.
Add: Blog No.1 & No.4 & No.5, Antongda Industrial Zone, 3rd Liuxian Road, Bao’an District, Shenzhen, 518101, China
Tel:+ 86 755 3688 7876
Fax:+ 86 755 3359 1582
sales@siglent.com
int.siglent.com
Headquarters