## Slide 1
SDS7000A High resolution Oscilloscope

## Slide 3
Contents
Basic information
Fundamental Functions
Advanced Functions
Competition Analysis

## Slide 4
PART ONE
01
Brief introduction
Every Bench. Every Engineer. Every Day.

## Slide 5
4GHz
220 μVrms
3GHz
180 μVrms
SDS7404A
SDS7304A
All Models
Sequence & History: 124,000 segments
15.6 ’ display capacitive touch screen
Net Weight 10.56 kg
Sample Rate: 20 GSa/s
Waveform capture rate: 1,000,000 wfm/s
Memory depth: 500 Mpts/ch,1 Gpts/ch (optional)
6GHz
260 μVrms
SDS7604A

## Slide 6
6 GHz bandwidth
  Faster rise time 68 ps
  More compliance tests possible
    DDR3
    1.5Gbps MIPI D-PHY
  Broaden the range of applications.
    Higher data speed can be tested
    Better signal integrity results
Bandwidth Upgrade

## Slide 7
Long time observation
  Capture more waveforms details.
  Ensure that the waveform is not distorted.
Excellent running performance
  Maintain a high sample rate.
  Accurate and effective analysis.
  1 Gpts/ch (Optional)
Memory depth = Sample rate x Sample time
500 Mpts deep Memory Depth

## Slide 8
More than 16 times the accuracy of 8-bit oscilloscopes
  Vertical resolution up to 16 bits in ERES mode.
  Conducive to the detection of small signals.
  Clearer and cleaner waveform display.
8-bit
12-bit
* 16 =
12-bit High Resolution

## Slide 9
Up to 1 million wfm/s
  Quickly capture abnormal or low probability events.
Higher Waveform Capture Rate

## Slide 10
Up to 20 GSa/s
  Avoid spectral aliasing.
  Rebuild the measured waveform precisely.
Excellent Real-time Sample Rate

## Slide 11
Upgrade to X86 processor
  32 GB DDR4, 250 GB SSD or better.
  Linux operating system.
  Greatly improve the system performance response speed.
Faster Processor

## Slide 12
New panel design, better touch
  15.6-inch HD touch screen.
  Fully consider the user's usage scenarios and habits.
Upgrade Of Touch Control

## Slide 13
Adjust Waveform Quickly

## Slide 14
10MHz IN
10MHz OUT
AUX OUT
EXT TRIGGER
OCXO
USB2.0 Device
AWG
More Interfaces & Extended Functions

## Slide 15
4 × USB Host 3.1 Gen 1
HDMI 1.4
DVI-D
Mic In
Line Out
Line In
2×1000M LAN
COM
DP 1.2

## Slide 16
PART TWO
02
Basic Functions
Every Bench. Every Engineer. Every Day.

## Slide 17
Split-screen Display
4 display windows
  Waveforms are more intuitive.
  15.6-inch capacitive touch HD display.

## Slide 18
Color Temperature Display Mode
Intuitively display the probability of waveform occurrence
  The higher the probability, the warmer the color.
  The lower the probability, the colder the color.

## Slide 19
Sequence Mode & History Mode
  Playback and observe unusual events at any time.
History
  The interval between segments can be as small as 0.9μs.
Sequence
Maximum of 124,000 frames can be recorded

## Slide 20
Search & Navigate
Search conditions: Edge, Slope, Pulse, Interval, Runt.
Navigate type: Search Event, Time, History Frame.

## Slide 21
Extensive Measurement Parameters
60+ different types of measurements
  4 categories: horizontal, vertical, delay and miscellaneous.
  Statistics: Current, Mean, Min, Max, Stdev, Count; Trend, Track, Histogram.

## Slide 22
Advanced Math Function
4 math traces are available
Formula Editor

## Slide 23
Hardware-accelerated FFT
32Mpts FFT operation
  Fast refresh rate
  Hardware-accelerated Save up to 88% of time
  High-frequency resolution
  SFDR as low as 45dBc

## Slide 24
Built-in Mask
80,000 Pass / Fail decisions each second
  Automatically take screenshots or save historical frames.
  Ideal for long-term signal monitoring or automated production line testing.
Hardware-based High Speed Mask Test Function

## Slide 25
Zone Trigger
Quickly isolate the waveform of interest
  Signals that are difficult to characterize.
  Two user-defined areas .
  Intersect or not intersect .

## Slide 26
PART THREE
03
Advanced Functions
Every Bench. Every Engineer. Every Day.

## Slide 27
Standard：I2C, SPI, UART, CAN, LIN
Optional：CAN FD, FlexRay, I2S, MIL-STD-1553B, SENT, Manchester, ARINC429,
    USB2.0
Serial Bus Decode

## Slide 28
Bode Plot
Obtain gain and phase values for each frequency point
  Power supply loop response analysis.
  Low frequency response analysis of passive filters and amplifier circuits.

## Slide 29
Power Analysis (Optional)
Conveniently measure 12 parameters such as power quality, harmonics, inrush current and switching loss.
Greatly improve the design efficiency of switching power supplies and power devices.

## Slide 30
Eye/Jitter Analysis (Optional)
Automatically extract the embedded reference clock from serial data
Mask test on eye diagrams.
Measurement on multiple eye/jitter parameters.

## Slide 31
Compliance Test(Optional)
USB 2.0, 100Base-TX, 1000Base-T, 100Base-T1, 1000Base-T1，MIPI-DPHY，DDR2/DDR3
  Connect the fixture according to the prompt.
  Test items can be completed quickly without manual measurement.
  Automatically generate reports.

## Slide 32
Digital Channels / MSO
Acquisition and analysis of mixed signals by 16 digital channels
  Reflect the timing relationship of the measured signal.
  Max. Sampling Rate: 1 GSa/s.
  Memory depth: 50 Mpts/ch.

## Slide 33
50 MHz Function/Arbitrary Waveform Generator(Optional)
Built-in
  Sampling Rate: 125 MSa/s
  Waveforms: Sine, Square, Ramp, Pulse, DC, Noise, 45 Arbitrary
Frequency Resolution: 1 μHz

## Slide 34
PART FOUR
04
Competition Analysis
Every Bench. Every Engineer. Every Day.

## Slide 35
 | Siglent SDS7000A |  | Keysight Infiniium EXR | 
Channels | 4 | X | 4/8 | √
Bandwidth | 3/4/6GHz | X | 500MHz 1/2/2.5/4/6GHz | √
Sample rate | 20 GSa/s (interleaving mode) 10 GSa/s (non-interleaving mode) | ○ | 16 GSa/s, all analog channels | ○
Vertical resolution | 12 bits, 16 bits(ERES) | √ | 10 bits, 16 bits(ERES) | X
Memory depth | 500 Mpts/ch | √ | 100 Mpts/ch | X
Waveform capture rate | 1,000,000 wfm/s | √ | 200, 000 wfms/s | X
Noise floor | 150uVrms @ 2 GHz BW 180uVrms @ 3 GHz BW 220uVrms @ 4 GHz BW 260uVrms @ 6GHz BW | X | 81uVrms @ 1 GHz 102uVrms @ 2 GHz 112uVrms @ 2.5 GHz 149uVrms @ 4GHz | √
DC gain accuracy | 1 mV/div ~ 4.95 mV/div: ±1.5% full scale(typical) 5 mV/div ~ 10 V/div: ±0.5% full scale(typical) | √ | ± 2% full scale (±1% typical) | √
Zone trigger | standard | √ | optional | X
Mask test | standard | √ | standard | √
Power analysis | optional | √ | optional | √
Eye test | optional | X | standard | √
Jitter test | optional | √ | optional | √
Display | 15.6 inch | √ | 15.6 inch | √
Wight | 10.56 kg | X | 13.75 kg | √

## Slide 36
 | Siglent SDS7000A |  | R&S RTO2000 | 
Channels | 4 | √ | 2/4 | √
Bandwidth | 3/4/6GHz | X | 600MHz 1/2/3/4/6GHz | √
Sample rate | 20 GSa/s (interleaving mode) 10 GSa/s (non-interleaving mode) | √ | max. 10 GSa/s on each channel R&S®RTO2044, R&S®RTO2064 max. 10 GSa/s (4 channels) max. 20 GSa/s (2 channels) | X
Vertical resolution | 12 bits, 16 bits(ERES) | √ | 8 bits, 16 bits(ERES) | X
Memory depth | 500 Mpts/ch | √ | 50 Mpts(4 channels) 100 Mpts(2 channels) 200 Mpts (1 channel) | X
Waveform capture rate | 1,000,000 wfm/s | √ | 1,000,000 wfm/s | √
Noise floor | 150uVrms @ 2 GHz BW 180uVrms @ 3 GHz BW 220uVrms @ 4 GHz BW 260uVrms @ 6 GHz BW | √ | 130uVrms @ 1GHz 200uVrms @ 2GHz 220uVrms @ 3GHz 260uVrms @ 4GHz | X
DC gain accuracy | 1 mV/div ~ 4.95 mV/div: ±1.5% full scale(typical) 5 mV/div ~ 10 V/div: ±0.5% full scale(typical) | √ | at 50 Ω, input sensitivity > 5 mV/div: ±1.5 % at 50 Ω, input sensitivity ≤ 5 mV/div: ±2 % at 1 MΩ: ±2 % | X
Zone trigger | standard | √ | optional | X
Mask test | standard | √ | standard | √
Power analysis | optional | √ | optional | √
Eye test | optional | X | standard | √
Jitter test | optional | √ | optional | √
Display | 15.6 inch | √ | 12.1 inch | X
Wight | 10.56 kg | X | 9.6 kg | √

## Slide 37
 | Siglent SDS7000A |  | LeCroy WavePro HD | 
Channels | 4 | √ | 4 | √
Bandwidth | 3/4/6GHz | X | 2.5/4/6/8GHz | √
Sample rate | 20 GSa/s (interleaving mode) 10 GSa/s (non-interleaving mode) | √ | 20 GSa/s (2 channels) 10 GSa/s (4 channels) | √
Vertical resolution | 12 bits, 16 bits(ERES) | √ | 12 bits, 15 bits(ERES) | X
Memory depth | 500 Mpts/ch | √ | 100 Mpts/ch | X
Waveform capture rate | 1,000,000 wfm/s | √ | unknown | 
Noise floor | 150uVrms @ 2 GHz BW 180uVrms @ 3 GHz BW 220uVrms @ 4 GHz BW 260uVrms @ 6 GHz BW | √ | 155uVrms @ 2.5GHz 228 uVrms @ 4GHz 285 uVrms @ 6GHz 315 uVrms @ 8GHz | √
DC gain accuracy | 1 mV/div ~ 4.95 mV/div: ±1.5% full scale(typical) 5 mV/div ~ 10 V/div: ±0.5% full scale(typical) | X | ± 0.5% full scale | √
Zone trigger | standard | √ | Not support | X
Mask test | standard | √ | standard | √
Power analysis | optional | √ | optional | √
Eye test | optional | √ | optional | √
Jitter test | optional | √ | optional | √
Display | 15.6 inch | √ | 15.6 inch | √
Wight | 10.56 kg | √ | 11.1 kg | X

## Slide 38
 | Siglent SDS7000A |  | Rigol DS70000 | 
Channels | 4 | √ | 4 | √
Bandwidth | 3/4/6GHz | X | 3/5GHz | √
Sample rate | 20 GSa/s (interleaving mode) 10 GSa/s (non-interleaving mode) | √ | 20 GSa/s (interleaving mode) 10 GSa/s (non-interleaving mode) | √
Vertical resolution | 12 bits, 16 bits(ERES) | √ | 8 bits 16 bits (ERES) | X
Memory depth | 500 Mpts/ch | √ | 500 Mpts(4 channels) | X
Waveform capture rate | 1,000,000 wfm/s | √ | 1,000,000 wfms/s | √
Noise floor | 150uVrms @ 2 GHz BW 180uVrms @ 3 GHz BW 220uVrms @ 4 GHz BW 260uVrms @ 6 GHz BW | √ | 600uVrms @3GHz BW 800 uVrms @ 5GHz BW | X
DC gain accuracy | 1 mV/div ~ 4.95 mV/div: ±1.5% full scale(typical) 5 mV/div ~ 10 V/div: ±0.5% full scale(typical) | √ | ± 2% full scale | X
Zone trigger | standard | √ | not support | X
Mask test | standard | √ | standard | √
Power analysis | optional | √ | not support | X
Eye test | optional | √ | optional | √
Jitter test | optional | √ | optional | √
Display | 15.6 inch | √ | 15.6 inch | X
Wight | 10.56 kg | √ | 22.5kg | X

## Slide 39
Model | Description
SDS7604A H12 | 6 GHz, 20 GSa/s, 4-CH, 12-bit, standard 500 Mpts/ch memory depth, 15.6” capacitive touch screen
SDS7404A H12 | 4 GHz, 20 GSa/s, 4-CH, 12-bit, standard 500 Mpts/ch memory depth, 15.6” capacitive touch screen
SDS7304A H12 | 3 GHz, 20 GSa/s, 4-CH, 12-bit, standard 500 Mpts/ch memory depth, 15.6” capacitive touch screen
Standard Accessories | Quantity
USB cable | 1
Quick start | 1
Passive probe (SP3150A) | 1/channel
Certificate of calibration | 1
Wireless mouse | 1
Power cord | 1
Protective Cover | 1
Ordering Information

## Slide 40
Optional Accessories | Part No. | Optional Accessories | Part No.
Waveform generator (software) | SDS7000A-FG | 100Base-TX compliance test (software) | SDS7000A-CT-100BASE-T
16 digital channels (software) | SDS7000A-16LA | 1000Base-T compliance test (software) | SDS7000A-CT-1000BASE-T
16-channel logic probe | SPL2016 | 100Base-T1 compliance test (software) | SDS7000A-CT-100BASE-T1
Power Analysis (software) | SDS7000A-PA | 1000Base-T1 compliance test (software) | SDS7000A-CT-1000BASE-T1
Power Analysis deskew fixture | DF2001A | Ethernet test fixture | FX-ETH
Eye Diagram/Jitter Analysis (software) | SDS7000A-EJ | Automotive Ethernet test fixture | FX-AMETH
I2S trigger & decode (software) | SDS7000A-I2S | 1Gpts memory depth（software） | SDS7000A-1GPTS
MIL-STD-1553B trigger & decode (software) | SDS7000A-1553B | STB3 demo signal source | STB3
FlexRay trigger & decode (software) | SDS7000A-FlexRay | USB-GPIB adapter | USB-GPIB
CAN FD trigger & decode (software) | SDS7000A-CANFD | OCXO timebase (Assembled and calibrated in factory only) | 10M_OCXO_L
SENT trigger & decode (software) | SDS7000A-SENT | High-speed active probe | SAP1000, SAP2500
Manchester decode (software) | SDS7000A-Manch | High voltage probe | HPB4010
ARINC429 trigger & decode (software) | SDS7000A-ARINC | High-speed differential probe | SAP2500D, SAP5000D
USB 2.0 decode (software) | SDS7000A-USB2 | High voltage differential probe | DPB1300/DPB4080/DPB5150/ DPB5150A/DPB5700/DPB5700A
USB 2.0 compliance test (software) | SDS7000A-CT-USB2 | Current probe | CPL5100/CP4020/CP4050/CP4070/CP4070A CP6030/CP6030A/CP6150/CP6500
USB 2.0 test fixture | FX-USB2 | Transit case | CASE-S2
3 GHz to 4GHz bandwidth upgrade(software) | SDS7000A-BW3T4 | 6 GHz to 8 GHz bandwidth upgrade (software) | SDS7000A-BW6T8

## Slide 41
SAP5000D Active Differential Probe
Bandwidth: 5 GHz
Attenuation ratio: 10：1
Rise time: 80ps
Vertical displacement range: ±12 V
Interface: SAPBus
Cable length: 130 cm

## Slide 42
USB 2.0 Compliance Test Fixture（FX-USB2 ）
USBTF_SQ
Controller
SQ Device
Droop
SQ Host
Sensitivity Recevier
Trigger
Inrush
USBTF_SR
Back Voltage
Droop

## Slide 43
100 Base-TX/1000Base-T
Compliance Test Fixture（FX-ETH ）
calibration section
SMA test section
Probe test section
MDI common-mode output voltage test
Disturbing test section
jitter test section
Link partner test section

## Slide 44
100 Base-T1/1000Base-T1
Compliance Test Fixture（FX-AMETH ）
Frequency converter test fixture
Automotive Ethernet test fixture
Automotive Ethernet Adapter(MateNet to SMA, Mini-50 to SMA, H-MTD to SMA)

## Slide 45
SIGLENT TECHNOLOGIES GERMANY GmbH
Add: Staetzlinger Str. 70 86165 Augsburg, Germany Tel: +49(0)-821-666 0 111 0 Fax: +49(0)-821-666 0 111 22 info-eu@siglent.com www.siglenteu.com
NA
SIGLENT Technologies NA, Inc.
Add: 6557 Cochran Rd Solon, Ohio 44139 Tel: 440-398-5800 Toll Free:877-515-5551 Fax: 440-399-1211
info@siglent.com www.siglentna.com
Every Bench. Every Engineer. Every Day.
Thank You
Europe
SIGLENT TECHNOLOGIES CO., LTD.
Add: Blog No.4 & No.5, Antongda Industrial Zone, 3rd Liuxian Road, Bao’an District, Shenzhen, 518101, China
Tel:+ 86 755 3688 7876
Fax:+ 86 755 3359 1582
sales@siglent.com
int.siglent.com
Headquarters