## Slide 1
www.siglent.com
EVERY BENCH. EVERY ENGINEER. EVERY DAY.
SIGLENT TECHNOLOGIES

## Slide 2
Why do customers need opt. Isolated Probes despite we have already solutions?
 Floating Measurements require special tools
Supply Voltage 600 V
600 V
615 V
15 V
HV Differential Probes
Isolated Channel Oscilloscope
Ground-free, floating Measurements

## Slide 3
New Semiconductors change the Requirements
Wide BandGap (WBG) Semiconductors (SiC / GaN) are key to improve efficiency of Power Electronics
WBG Semiconductors help to satisfy the market requirements.

## Slide 4
WBG Semiconductors:
Effects on Measurements and Equipment
Silicon-based vs. WBG-Semiconductors
  Faster Rise/Fall times
  Faster Switching Speed
  Higher DI/Dt
  Higher DV/Dt
Which T&M requirements are affected?
  Bandwidth for Voltage and Current measurements
  EMC
  Dynamic Range
  Common Mode Rejection Ratio (CMRR @ higher Frequencies)
  Probing
700V
3.3kV
10kV
100ns
10ns
1ns
<1ns
IGBT
SiC
GaN
Silicon
Rise Time
Differential Voltage

## Slide 5
Comparison Classic vs. Opt.Iso.Probe
Source: Wolfspeed App.Note, Dynamic Characterization and Measurement Methods
Differential Amplifier
+
-
Common Mode Error @100MHz with HV-Diff. Probe
CMMR = 25 dB ~ 18:1
600V / 18 = 33,3V
VCM 600 V
Vdiff 15 V
Classical HV-diff. Probe
Opt. Iso. HV-diff. Probe
Faster Rise time need Higher Bandwidth Scope & Probes
Current Siglent Solutions: limited to 200 MHz

## Slide 6
Whom should we address with the Siglent Solution?
Fokus Area
Notes: Semiconductor Manufactureres mostly have solutions. Same is valid #
End customers mainly buy ready to use devices and maximum do verification tests.

## Slide 7
ODP6000A

## Slide 8
Ordering Information
Model | Description | List Price
ODP6050B | Optical isolated probe: 500 MHz, 50X, Max. Differential Test Voltage (DC + Peak AC) +/-25 V, Isolated Voltage +/-60 kV, DC 5 V adapter or 7.4 V battery Power supply, Standard attenuators 50X/1000X/2000X/5000X | € 4.500
ODP6100B | Optical isolated probe: 1 GHz, 50X, Max. Differential Test Voltage (DC + Peak AC) +/-25 V, Isolated Voltage +/-60 kV, DC 5 V adapter or 7.4 V battery Power supply, Standard attenuators 50X/1000X/2000X/5000X | € 8.530
CK-AT5X-2 | Connector Type SSMB, Attenuation Ratio 5:1，Measurement Range ±2.5 Vpk, Input Impedance 1 MΩ¦¦28 pF | € 173
CK-AT10X-2 | Connector Type SSMB, Attenuation Ratio 10:1，Measurement Range ±5 Vpk, Input Impedance 1 MΩ¦¦6 pF | € 173
CK-AT20X-2 | Connector Type SSMB, Attenuation Ratio 20:1，Measurement Range ±10 Vpk, Input Impedance 5 MΩ¦¦6 pF | € 173
CK-AT50X-2 | Connector Type SSMB, Attenuation Ratio 50:1，Measurement Range ±25 Vpk, Input Impedance 10 MΩ¦¦4 pF | € 173
CK-AT100X-2 | Connector Type SSMB, Attenuation Ratio 100:1，Measurement Range ±50 Vpk, Input Impedance 10 MΩ¦¦2 pF | € 173
CK-AT200X-2 | Connector Type SSMB, Attenuation Ratio 200:1，Measurement Range ±100 Vpk, Input Impedance 10 MΩ¦¦2 pF | € 173
CK-AT500X-2 | Connector Type 2.54 mm socket, Attenuation Ratio 500:1, Measurement Range ±250 Vpk, Input Impedance 10 MΩ¦¦2 pF | € 288
CK-AT5X-2 | Connector Type SSMB, Attenuation Ratio 5:1，Measurement Range ±2.5 Vpk, Input Impedance 1 MΩ¦¦28 pF | € 173

## Slide 9
EVERY BENCH. EVERY ENGINEER. EVERY DAY.