## Slide 3
SSA5000A Spectrum Analyzer
SSG5000A RF Signal Generator
Contents
SSA5000A introduction
SSG5000A introduction
Competition Analysis
Applications

## Slide 4
SSA5000A main parameters and options
 | SSA5083A | SSA5085A
Frequency range | 9 kHz ~ 13.5 GHz | 9 kHz ~ 26.5 GHz
Displayed Average Noise Level | -165 dBm/Hz | 
SSB Phase Noise | <-105 dBc/Hz @1 GHz, offset 10 kHz | 
Analysis Bandwidth | 25 MHz, 40 MHz(opt.) | 
Screen | 12.1 inch touch screen | 
Options |  | 
SSA5000-AMK | Power Measurement: CHP, Channel Power, ACPR, OBW, T-Power, CNR; Non-Linear Measurement: Harmonic measurement, TOI; Spectrum Monitor Measurement: Spectrogram | 
SSA5000-AMA | Analog Modulation Analysis: AM, FM, PM | 
SSA5000-DMA | Digital Modulation Analysis: ASK, FSK, MSK, PSK, DPSK, QAM | 
SSA5000-RTA1 | Real-Time Spectrum Analysis: 25 MHz analysis bandwidth | 
SSA5000-B40 | 40 MHz analysis bandwidth (RTA1 option required) | 
SSA5000-P3 | Pre-amplifier, 9 kHz ~ 13.6 GHz | 
SSA5000-P5 | Pre-amplifier, 9 kHz ~ 26.5 GHz | 
SSA5000-F5 | SSA5083A upgrade to SSA5085A | 
SSA5000-EMI | EMI measurement mode | 
10M_OCXO_L | OCXO Precise Reference source, Factory installed | 

## Slide 5
2.92 mm male
RF OUTPUT
2.92F-2.92F connector
Mouse and Keyboard , Storage
12.1‘’ touch screen

## Slide 6
Quick settings of frequency range, RBW, SPAN
Main menus
Modes switch
Undo, Redo, Marker, Save/Recall, Log file, Trace, Trigger, Attenuation

## Slide 7
Webserver,
More commands than SSA3000X
HDMI output, easy demonstration
High accuracy clock source, factory installed only
10 MHz IN/OUT,
TRIG IN/OUT

## Slide 8
SSA5000A competition analysis
 | SSA5000A | R&S FSL (Discontinued) | Keysight N9323/4C
Frequency Range | 9 kHz ~ 13.6/26.5 GHz | 9 kHz ~ 3/6/18 GHz (overrange 20 GHz) | 1 MHz to 13.6/20 GHz
RBW | 1Hz ~ 10MHz | 300 Hz to 10 MHz; 10 Hz to 10 MHz(R&S®FSL-B7 option) | 10 Hz to 3 MHz
Analysis Bandwidth | Standard 25 MHz, 40 MHz (opt. SSA5000-B40) | Not support | Not support
Displayed average noise level (DANL) | - 165 dBm/Hz best | - 152 dBm/Hz best | - 156 dBm/Hz best
Amplitude Measurement Range | Preamp off: DANL ~ +10 dBm, 100 kHz ~ 1 MHz; DANL ~ +23 dBm, 1 MHz ~ 26.5 GHz | Displayed noise floor to +20 dBm | Preamp off: 1 MHz to 500 MHz DANL to +10 dBm; 500 MHz to 20 GHz DANL to +20 dBm
Storage | Internal (eMMC) 4 GB, external (USB storage device) 32 GB | flash disk (internal), USB memory stick | Internal 64 MB nominal, USB memory devices external
Screen | 12.1 inch TFT-LCD touch screen,1280*800 | 5.8 inch, 640*480 | 6.5 inch touch screen, 640*480
Weight | Net: 7.40 kg | with battery pack < 8 kg | Net 7.9 kg; Shipping 14.5 kg
Dimensions | 378 mm x 284 mm x 126 mm (W×H×D) | 408.8 mm × 158.1 mm × 465.3 mm | 320 mm × 132.5 mm × 400 mm
Price | SSA5083A US$ 18,880; | FSL18 21569 € incl PreAmp | N9323C US$ 17,879;
 | SSA5085A US$ 21,880; |  | N9324C US$ 20,057;
Notes: SSA5000A is in the same price range of FSL, N9323/4C.
SSA5000A has a modern design features light weight and portability.
SNA5000A has better specifications

## Slide 9
SSG5000A main parameters and options
 | SSG5083A | SSG5085A
Frequency range | 9 kHz ~ 13.6 GHz | 9 kHz ~ 20 GHz
Frequency resolution | 0.001 Hz | 
Amplitude resolution | 0.01 dB | 
Level setting range | -130 dBm to + 25 dBm | 
Level error | ≤ 0.7 dB(typ.) | 
Phase noise | -120 dBc/Hz @1 GHz, offset 20 kHz (typ.) | 
Clock source | Standard high accuracy 10M_OCXO_L | 
Screen | 5 inch capacitance touch screen, RGB (800*480) | 
Options |  | 
SSG5080A-PU | Pulse modulation | 
SSG5080A-PT | Pulse train generator | 
SSG5080A-LP | 110dB Attenuator module (Assembled and calibrated in factory only) | 
SSG-RMK | Rack mount kit | 
SSG5080A-F85 | Upgrade 13.6 GHz to 20 GHz | 
USB-GPIB | USB-GPIB adapter | 

## Slide 10
SSG5000A competition analysis
 | SSG5000A | Keysight N5173B
Frequency Range | 9 kHz ~ 13.6/20 GHz | 9 kHz to 13/20/31.8/40 GHz
Frequency resolution | 0.001 Hz | 0.001 Hz
Max output power | 9 kHz ≤f＜100 kHz, +3 dBm; 100 kHz ≤f＜1 MHz, +15 dBm; 1 MHz ≤f≤4 GHz, +24 dBm; 4 GHz <f≤6 GHz, +21 dBm; 6 GHz＜f≤15 GHz, +20 dBm; 15 GHz＜f≤20 GHz, +15 dBm | 9 kHz to 3.2 GHz, 18 dBm; 3.2 to 13 GHz, 18 dBm; 13 to 20 GHz, 15 dBm
Maximum reverse power | 1 MHz≤f≤6 GHz, 30 dBm; 6 GHz≤f≤20 GHz, 25 dBm; 50 Vdc | 0.5 W, 0 Vdc
SSB phase noise (dBc/Hz) | at 20 kHz offset: 100 MHz, -122; 1 GHz, -120; 4 GHz, -106; 6 GHz, -105; 10 GHz, -99; 20 GHz, -93 | at 20 kHz offset: 5 to < 250 MHz, –115; 250 MHz, –129; 500 MHz, –124; 1 GHz, –118; 2 GHz, –111; 3 GHz, –105; 4 GHz, -104; 6 GHz, -99; 10 GHz, -97; 20 GHz, -90
AM/FM/PM | Standard | Option N5173B-UNT, $4739
Internal pulse generator | Standard | Option N5173B-UNW, $6801 (narrow pulse modulation)
Screen | 5'' touch screen | Not mentioned
Weight | 6.1 kg net | 14.5 kg net, 29.5 kg shipping
Dimensions | W×H×D=338×113×369 mm | 426 mm W x 88 mm x 489 mm L
Price | SSG5083A, $16,990; SSG5085A, $19,990; SSG5080A-PU, $2,380; SSG5080A-PT, $2,380; SSG5080A-LP, $4,590 | N5173B-513, $24,266； N5173B-520, $28,154; Option N5173B-UNW, $6,801 (narrow pulse modulation); N5173B-1E1 (Step attenuator, 115 dB), $5,634
Notes: Conclusion: 1) Siglent SSG5000A is a more modern signal generator. It's only 40% the weight of N5173B and occupys 40% less of the desk space. A 5'' touch screen with dedicated UI boosts efficiency to a great extent. 2) With a wider max output power, SSG5000A covers wider application areas. The ability to withstand larger reverse power protect customer investment from accidents. 3) A better SSB phase noise and lower subharmonics make SSG5000A performs better in higher frequency ranges. Common functions like AM/FM/PM, pulse generator are all standard on SSG5000A. It saves customer money and engineers care no chores like installation of options.

## Slide 11
Applications
Radar
Quantum physics
Communication
Components verification

## Slide 12
Applications – Components evaluation
SSG5000A can be used as high frequency LO
SSA5000A performs modulation analysis
SSG5000X-V is baseband generator
Upconverter
SPD3303X-E
Power Supply
SSA5000A
Spectrum Analyzer
SSG5000A
LO INPUT
SSG5000X-V
BASEBAND INPUTS
DC
GND
I+
I-
Q+
Q-
RF out

## Slide 13
Applications – Components evaluation

## Slide 14
SIGLENT TECHNOLOGIES GERMANY GmbH
Add: Liebigstrasse 2-20, Gebaeude 14, 22113 Hamburg Germany Tel: +49(0)40-819-95946
Mobile: +49 151 40716756 Fax: +49(0)40-819-95947 info-eu@siglent.com www.siglenteu.com
NA
SIGLENT Technologies NA, Inc.
Add: 6557 Cochran Rd Solon, Ohio 44139 Tel: 440-398-5800 Toll Free:877-515-5551 Fax: 440-399-1211
info@siglent.com www.siglentna.com
The Best Value in Electronic Test & Measurement
Thank You
Europe
SIGLENT TECHNOLOGIES CO., LTD.
Add: Blog No.4 & No.5, Antongda Industrial Zone, 3rd Liuxian Road,
Bao’an District, Shenzhen, 518101, China.
Tel:+ 86 755 3688 7876
Fax:+ 86 755 3359 1582
sales@siglent.com
www.siglent.com/ens
Headquarters